## Slide 1
Model-Based-Design workflow using the Inverted Pendulum Problem
Mr. Sebastien Dupertuis
Applications Engineer
Wednesday, March 11, 2015
Notes: Feel free to adapt the table of contents and hide slides based on what you are going to show or not.
The Readme.docx file gives a good overview of what should be shown and what is optional.

## Slide 2: Three Key Takeaways
From one model to many targets using MATLAB and Simulink
Automatic code generation out of an executable specification
Bi-directional traceability between requirements, models and generated code

## Slide 3: Topics
Introduction
  Problem formulation
  Base model and project overview
Plant modelling
  Introduction to SimMechanics
  Modelling the inverted pendulum
Control logic modelling
  Introduction to Stateflow
  Controller modelling and analysis
Control design
  PID tuning
  System identification
Code generation and verification
  Automatic code generation
  In-the-Loop verification methodologies

## Slide 4: Problem Formulation Inverted pendulum
Plant Differential Equation:

## Slide 5: Base Model Overview
Notes: Demo: open the final model, run it, show SM 3D visualization as well as scope; explain shortly the blocks on the top-level

## Slide 6: Integrated Development Environment Simulink Project

## Slide 7: Use of Simulink Projects
Organize the structure of project’s folders and files
Put all source files and models under version control
Have an overview of files relationship
Share project’s data among the team
Do automation of tasks
Notes: Simulink Projects is an interactive tool in Simulink for managing your project files and connecting to source
control software. It promotes effective collaboration across teams.
Using Simulink Projects gives the possibility to the team to get benefits of standard IDEs with integrated
version control system and allows team members to get a good overview of the entire projects.

## Slide 8: Simulink Projects: main advantages
Support team work
  Design reuse
  Parallel workflows
  Source control integration
  Knowledge transfer across projects
Setup guidelines
  Team members work the same way
  Teams leaders get accurate projects overview
  Projects integrity is stable and under control at any time

## Slide 9: Configuration Management
Simulink Projects supports:
Subversion (SVN) integration by default
Git
Use of the Source Control Adapter SDK to link to another Source Control System
Notes: Simulink Projects do integrate Source Control System. By default, SVN is defined as the standard Version
Control System for Simulink Projects. However, the Version Control System “Git” is also supported by
Simulink Projects. If another Source Control System is commonly used in the company, it can be linked to
Simulink by using the Source Control Adapter SDK.

## Slide 10: Configuration Management: Subversion
Notes: Here is the representation of the SVN Architecture:
On the server side, there are the SVN repositories related to different projects inside the company that are interfaced with either the Subversion Server or the CollabNet Subversion Server. Subversion Server: it runs the simple svn protocol which is not WebDAV compliant. WebDAV stands for Web Distributed Authoring and Versioning. It is an extension of the Hypertext Transfer Protocol (HTTP) that facilitates collaboration between users in editing and managing documents and files stored on World Wide Web servers. CollabNet Subversion Edge: it runs the HTTP/HTTPS protocols which are WebDAV compliant. This also allows users to get access to the Web Viewer Interface for Subversion repositories. This gives the possibility to team leaders to get an overview of a specific project by navigating through its different files directly online without having to create locally a working copy of the project.
On the client side, there are the working copies related to the different projects located on the SVN repositories. They are directly controlled by the SVN command line client which can be driven by a graphical interface like TortoiseSVN. The exchange of data between the clients and the server can be done via the svn or http/https protocols, or locally if the Subversion Server is installed on the same computer.
For the setup of the Hardware on the network, their are:
The server running CollabNet Subversion Edge plus its Backup Server which can process nightly builds of every repositories in order to check the integrity of them. The Server can be setup so that it serves data over either an HTTP or HTTPS connections depending on the network that is used by the team members

## Slide 11: Configuration Management: Typical Workflow

## Slide 12: Integrated Development Environment Simulink Data Dictionary

## Slide 13: Data Management Capabilities
Change tracking and differencing
Defined relationship with SLDD file
Componentization
Scalability and performance
Integration with Simulink Projects
Provides management for global design data:
Simulink
SLX
File
SLX
File
Model 1
Model 2
Model 3
SLX
File
SLDD
File
SLDD
File
SLDD
File
Global Data

## Slide 14: Data Management: Migration

## Slide 15: Data Management: Change Tracking

## Slide 16: Topics
Introduction
  Problem formulation
  Base model and project overview
Plant modelling
  Introduction to SimMechanics
  Modelling the inverted pendulum
Control logic modelling
  Introduction to Stateflow
  Controller modelling and analysis
Control design
  PID tuning
  System identification
Code generation and verification
  Automatic code generation
  In-the-Loop verification methodologies

## Slide 17: Introduction to SimMechanics
Simulate and visualize 3D multibody mechanical systems
Construct model using rigid bodies, joints, and forces
  Model matches structure of system
  No need to derive and program equations
Primary uses
  System-level dynamics analysis
  Control development in Simulink
SimMechanics
SimDriveline
SimHydraulics
SimElectronics
SimPowerSystems
Simscape
MATLAB, Simulink

## Slide 18: Modelling Concepts
Simscape: Multi-Domain Modelling  Energy flow dynamics
SimMechanics: Multibody mechanical model  What is relevant?
Mechanical dynamics – location, movement
Block ports represent coordinate systems
Blocks are bodies or coordinate transforms
Forces/torques are applied to joints

## Slide 19: Building the Pendulum in SimMechanics

## Slide 20: Pendulum

## Slide 21: Topics
Introduction
  Problem formulation
  Base model and project overview
Plant modelling
  Introduction to SimMechanics
  Modelling the inverted pendulum
Control logic modelling
  Introduction to Stateflow
  Controller modelling and analysis
Control design
  PID tuning
  System identification
Code generation and verification
  Automatic code generation
  In-the-Loop verification methodologies

## Slide 22: Introduction to Stateflow: Terms
Chart: A Stateflow chart that contains either
  State diagrams: A chart that contains State(s)
  Flow charts: A chart that does not use State(s), only transitions and conditional logic. NOTES: most Stateflow charts use a mixture of State diagrams and Flow Charts
Stateflow Functions: discrete functions that can be called from within the Stateflow diagram
  Graphical functions
  Simulink functions
  MATLAB functions

## Slide 23: Introduction to Stateflow: Terms
Level: a level is a grouping of Stateflow charts that is visible at one time. It can include nested Stateflow charts
  Subcharted states form a new level

## Slide 24: Introduction to Stateflow: States
In the following example, drawing one state within the boundaries of another
state indicates that the inner state is a substate (or child) of the outer state (or
superstate). The outer state is the parent of the inner state:
Stateflow hierarchy can also be represented textually, in which the Stateflow chart is represented by the slash (/) character and each level in the hierarchy of states is separated by the period (.) character
/Car_done
/Car_done.Car_made
/Car_done.Car_shipped
/Car_done.Car_made.Parts_assembled
/Car_done.Car_made.Painted

## Slide 25: Introduction to Stateflow: States
State Actions: After the name, you enter optional action statements for the
state with a keyword label that identifies the type of action. You can specify
none, some, or all of them. The colon after each keyword is required. The
slash following the state name is optional as long as it is followed by a
carriage return.
Entry Action. Preceded by the prefix entry or en for short. In the preceding example, state On has entry action on_count=0. This means that the value of on_count is reset to 0 whenever state On becomes active (entered).
During Action. Preceded by the prefix during or du for short. In the preceding label example, state On has two during actions, light_on() and on_count++. These actions are executed whenever state On is already active and any event occurs.
Exit Action. Preceded by the prefix exit or ex for short. In the preceding label example, state Off has the exit action light_off(). If the state Off is active, but becomes inactive (exited), this action is executed.
On Event_Name Action. Preceded by the prefix on event_name, where event_name is a unique event. In the preceding label example, state On has an on power_outage action. If state On is active and the event power_outage occurs, the action handle_outage() is executed.
Bind Action. Preceded by the prefix bind. In the preceding label example, the data on_count is bound to the state On. This means that only the state On or a child of On can change the value of on_count. Other states, such as the state Off, can use on_count in its actions, but it cannot change its value in doing so.

## Slide 26: Introduction to Stateflow
entry:
during:
exit:
Initialization: {}
Condition: []

## Slide 27: Controller
Logic
PID

## Slide 28: Controller Simple state machine
In this diagram | In Stateflow
’ | dTheta
Torque | Torque
Variables correspondence
In this diagram | In Stateflow
±Torque | ±TORQUE_LEVEL
Values correspondence
In this diagram | In Stateflow
No Torque | Torque = 0
Variables initialization

## Slide 29: Controller Simple state machine

## Slide 30: Controller Full state machine
In this diagram | In Stateflow
’ | dTheta
 | Theta
Torque | Torque
PID ON/OFF | Enable_Controller
Variables correspondence
In this diagram | In Stateflow
±Torque | ±TORQUE_LEVEL
WAIT | THETA_WAIT
SWING | THETA_SWING
BALANCING | THETA_BALANCING
Values correspondence
Trigger signal generation
In this diagram | In Stateflow
No Torque | Torque = 0
PID OFF | Enable_Controller = 0
Variables initialization

## Slide 31: Controller Full state machine

## Slide 32: Controller Coverage Analysis

## Slide 33: Topics
Introduction
  Problem formulation
  Base model and project overview
Plant modelling
  Introduction to SimMechanics
  Modelling the inverted pendulum
Control logic modelling
  Introduction to Stateflow
  Controller modelling and analysis
Control design
  PID tuning
  System identification
Code generation and verification
  Automatic code generation
  In-the-Loop verification methodologies

## Slide 34: Inverted pendulum: PID Tuning
TUNE

## Slide 35: PID Tuning

## Slide 36: PID Tuning
Set enough time:
SIM time = 200s
LIN time = 200s

## Slide 37: System identification App
>> ident

## Slide 38: System identification: Inverted Pendulum Non linear fit
State space representation:
Plant Differential Equation:

## Slide 39: Non linear fit of measurements data

## Slide 40: Grey box implementation of a non linear fit

## Slide 41: Topics
Introduction
  Problem formulation
  Base model and project overview
Plant modelling
  Introduction to SimMechanics
  Modelling the inverted pendulum
Control logic modelling
  Introduction to Stateflow
  Controller modelling and analysis
Control design
  PID tuning
  System identification
Code generation and verification
  Automatic code generation
  In-the-Loop verification methodologies

## Slide 42: Code Generation and Verification Variant Subsystems

## Slide 43: Code Generation and Verification S-Function, SIL/PIL

## Slide 44: Code Generation and Verification Simulation Data Inspector

## Slide 45: Three Key Takeaways
From one model to many targets using MATLAB and Simulink
Automatic code generation out of an executable specification
Bi-directional traceability between requirements, models and generated code